## Slide 1
RESPONDING TO COACH FEEDBACK
Reframing the Fault Classifier:
From Instant Recognition to Forecasting
Bolt — Vehicle Fault Diagnosis & Repair Copilot · Harsha, Ghada & Hüseyin
Notes: Hi everyone — quick walkthrough of a change we made to the classifier this week, based on feedback from our coach. Short version: our original results looked suspiciously perfect, our coach caught the actual reason why, and we fixed it properly instead of arguing around it. I'll walk through what we had, what he said, what we changed, and where that leaves us.

## Slide 2
WEEK 1-2 RECAP
Where we started
We trained a classifier on hourly EV sensor data to predict a Fault_Label
(Normal / Warning / Fault) for each row — treating every hour as its own, independent sample.
The setup
175,200 rows · 4 EVs × 5 years, hourly
Severe imbalance: Normal 98.37% / Fault 1.51% / Warning 0.12%
Chronological, per-vehicle train/test split
Random Forest + XGBoost, class-weighted
The result
1.000
macro F1 — Random Forest, including every single Warning-class row
XGBoost: 0.985 — close, but not perfect
2
Notes: Quick recap of where we were. We had a 175,000-row dataset, 4 simulated EVs over 5 years of hourly telemetry, and we trained Random Forest and XGBoost to classify each individual hour as Normal, Warning, or Fault. Random Forest came back with a perfect 1.000 macro F1 — it caught every single Warning row in the test set too. That number should make anyone suspicious, and it made us suspicious too — which is exactly what we brought to our coach.

## Slide 3
THE COACH'S FEEDBACK
“The data description suggests the end user installs measurement devices for hourly readings. This seems like 4 separate time-series problems, not a classification task... Please realign your business goal and metric accordingly.”
— Coach review, Week 2
In plain terms: we had been treating each hour as an independent sample. But 4 vehicles logged hourly over 5 years is 4 continuous time series — adjacent hours are related, and a model that only looks at one instant is solving an easier, less realistic problem.
3
Notes: Here's exactly what he said. In plain terms: he's pointing out that we have 4 vehicles logged hourly for 5 years — that's 4 continuous time series, not 175,000 unrelated data points. Treating each hour as its own independent sample throws away the fact that an hour is related to the hours around it. That's a real methodological gap, not a nitpick.

## Slide 4
CHECKING THE CLAIM
Why he was right
Straight from the dataset's own Kaggle page — its stated intended use cases:
“Multivariate time-series forecasting (e.g., CNN + LSTM models)”
“DTC forecasting and anomaly detection”
“Predictive maintenance modeling”
Row-level classification is not on that list.
We also checked the dataset's Kaggle Code and Discussion tabs directly — both show 0. No one has published an approach to compare against; this reframe had to be worked out from first principles.
It also fits our fleet-manager persona better: “is it safe to keep driving?” is inherently a question about what's about to happen — not what already happened.
4
Notes: We didn't just take his word for it — we checked. The dataset's own README lists its intended use cases, and forecasting and anomaly detection are explicitly on that list; row-level classification isn't. We also checked if anyone else had published a notebook on this dataset — zero. So there was no existing approach to lean on, we had to reason this through ourselves. And it lines up with our own fleet-manager persona too — 'is it safe to keep driving' is a forward-looking question by nature.

## Slide 5
THE FIX
What we changed
1
New features: recent history, not just the current instant
Rolling mean/std (6h/12h/24h), lags (1h/3h/6h), and trend deltas on Motor_RPM, Motor_Torque, Motor_Temp, Battery_Temp — computed strictly within each vehicle's own timeline.
2
New target: forecast ahead, not describe the present
Fault_Within_6h — will a fault occur in the next 6 hours? — instead of “is a fault happening right now?” Hand-verified against a brute-force check before trusting it on the full dataset.
3
Same discipline as before, carried forward
Same dataset, same chronological per-vehicle split, same class-weighting-from-training-fold-only rule. No SMOTE, no shortcuts — just a fairer task.
5
Notes: So here's exactly what changed, concretely. First, we added rolling and lag features — instead of just the current hour's reading, the model now sees the recent trend, computed separately per vehicle so we never mix one vehicle's history into another's. Second, we changed the target itself — instead of labeling 'is this hour a fault,' we now ask 'will a fault happen in the next 6 hours.' That's the actual forecasting reframe. Everything else — the dataset, the split, the class weighting — stayed exactly the same. This is a fix to the framing, not a restart.

## Slide 6
THE HONEST NUMBER
Results: before vs. after
Chart: Macro F1 — instant classification vs. forecasting
| Random Forest (instant) | XGBoost (instant) | Random Forest (forecast 6h) | XGBoost (forecast 6h)
Macro F1 | 1 | 0.985 | 0.599 | 0.594
Why a worse score
is the right outcome
The 1.000 score wasn't measuring a hard problem — it was recognizing a code using the same instant's readings that generated it.
~0.60 is a real, honest baseline for a genuinely hard forecasting task.
Recall on catching an upcoming fault: ~99% → ~46-59% — a large, expected drop, not a bug.
6
Notes: Here's the headline comparison. Macro F1 dropped from around 1.000 and 0.985 down to about 0.60 and 0.59. On paper that looks like a worse result — but it's actually the correct outcome. The original perfect score wasn't measuring anything hard; it was just recognizing a code using the exact same instant of data that generated it. This new 0.60 is a real, honest number on a genuinely difficult forecasting problem — recall on catching an upcoming fault dropped from about 99% to somewhere between 46 and 59%, which tells us there's real room to improve, and that's a much more trustworthy starting point to build on.

## Slide 7
TESTING OUR OWN ASSUMPTIONS
One more check, just to be sure
The hypothesis
Two features (Brake_Pad_Wear, SOH) suddenly looked important for the new target. We suspected this was a fake signal — a proxy for “which vehicle is this” rather than real predictive value.
Tested with:
Permutation importance on the trained model
Per-vehicle mutual information (removes “which vehicle” as a factor entirely)
The result
We were wrong — and we're saying so. Per-vehicle relevance came back higher than the pooled value, for every vehicle. That means it's real, genuine signal, not a confound.
The takeaway we're carrying forward: test a hypothesis with the same rigor as the original finding — don't just assume your first guess was right.
7
Notes: One more thing worth mentioning, because it shows how we're approaching rigor generally, not just on this one issue. When we reframed the task, two features suddenly looked important that hadn't before — Brake_Pad_Wear and SOH. Our first guess was that this was a fake signal, just a stand-in for which vehicle it is. So we tested that guess directly with permutation importance and per-vehicle mutual information. And the test disagreed with us — the signal turned out to be real, not a confound. We're bringing this up because we think it's important to show we test our own assumptions, not just assume our first read is correct.

## Slide 8
WHAT'S NEXT
This is a real starting point, not a finished result
Try the 12-hour forecast window — more positive examples to learn from
Try a small neural net on the same rolling/lag feature set
Follow up on Tire_Pressure / Charging_Voltage — the features the model actually leans on
Everything else (RAG, agent orchestration, dashboard) proceeds unaffected — this was a classifier-only fix
8
Notes: So where does this leave us. This 0.60 macro F1 is a real, honest baseline, not a finished result — we've got clear next steps: try a longer forecast window since it gives us more positive examples, try a small neural net on the same features, and dig into why the model actually leans on tire pressure and charging voltage instead of the features we expected. And importantly — this was a fix contained entirely to the classifier. RAG, the agent, and the dashboard all proceed exactly as planned, nobody's timeline was affected. That's it — happy to take questions.